## Slide 1: EDUp FORDCS V1.0 Software Development & Testing
Vienna, April.2022
MSc. Ömer Karacan
karacankos@gmail.com
Edu Platform
v2022.04
FORDSC Project
F
Compendium

## Slide 2: SwPD Method Epics - Setting Copy
Source: EDUp-Full-Stack-Software-Project-Development-Method.pptx

## Slide 3
System Requirements

## Slide 4: System Boundary - Illustrated
Ref.: FORDCS-V1.0 Customer requirements
Ref.: SmartHome_ConceptSpecificationSimplified_v2022.1.docx

## Slide 5: FORDCS-V1.0 System States
Ref.: FORDCS-V1.0 Customer requirements

## Slide 6: System Use Cases Use Case Report Factory Setting V1.0
Following scenario is assumed:
  ASSUMPTION: Any Actors may retrieve the Data from the FORDCS!
  Use Case should be implemented referring to the Swagger interface design: https://app.swaggerhub.com/apis/karacankos/fordcs/1.0-oas3
 Method-Note: The Customer Use Case Scenario is to be described per scenario from the viewpoint of System Architect

## Slide 7: System Use Cases Use Case Run-time Status Report V1.0
Following scenario is assumed:
  ASSUMPTION: ONLY the following Actors may receive the Data from the FORDCS:
    “Home resident”, “Charging Station System Operator”, “Building Technology System Operator”, and “BEA”!
  Use Case should be implemented referring to the Swagger interface design: https://app.swaggerhub.com/apis/karacankos/fordcs/1.0-oas3
 Method-Note: The Customer Use Case Scenario is to be described per scenario from the viewpoint of System Architect

## Slide 8: System Use Cases Use Case Starting-up the CS V1.0
Following scenarios are assumed:
  “Operational Readiness”:
    CS is installed, passed the “operational readiness test”, and the state is set to “INITIAL_STATE” via the configuration parameter “Status” by the “Charging Station System Operator” [REF_SHC]  CS State : INITIAL_STATE
  “Close the Power Circuit”:
    Via SmartMeter, the CS is connected to grid power, and the state is set to “UX_POWER_PRESENT” by the “Charging Station System Operator”!  CS State : UX_POWER_PRESENT
  “Connecting to Powerline”:
    CS is connected to the powerline, and the state is set to “POWER_OFF” via the configuration parameter “Status” by the “Charging Station System Operator” [REF_SHC]  CS State : POWER_OFF
System Use Case
Starting-up the CS V1.0
Notes: Method-Note:
The Customer Use Case Scenario is to be described per scenario from the viewpoint of System Architect

## Slide 9: System Use Cases Use Case Starting-up the CS V1.0
  “Charge the Car” [REF_SHC]:
    The “SystemControllerUnit” sets the state to “UX_ READY_TO_CHARGE”  CS State : UX_ READY_TO_CHARGE
  “Start charging”:
    The “Home resident” [REF_SHC] starts the charging!.
  “Stop charging”:
    The “Home resident” [REF_SHC] or the “SystemControllerUnit” stops the charging!.
  “Connect the Plug to Vehicle”:
    The “Home resident” [REF_SHC] connects the CS to the vehicle!
  “Disconnect the Plug from Vehicle”:
    The “Home resident” [REF_SHC] disconnects the CS from the vehicle!
System Use Case
Starting-up the CS V1.0

## Slide 10: System Use Cases Use Case Failure Handling V1.0
  “Failure Detection”:
    The “SystemControllerUnit” sets the state to “UX_ TROUBLE” and starts the system failure handling routine!  CS State : UX_ TROUBLE
System Use Case
Failure Handling V1.0

## Slide 11: System Requirements
SREQ_1: The Actors should be authorized to involved in specific system interactions!  Service-based authorization should be given!
SREQ_2: The service interfaces should be implemented as given (Swagger design)!
SREQ_3: The system should catch any failure and time and handle it!
Notes:  Method note:
Describe each REQ in a paragraph!

## Slide 12: System Boundary, Interfaces, and Users

## Slide 13: Assumptions

## Slide 14: References
[REF_SHC] … SmartHome_ConceptSpecificationSimplified_v2022.1.docx
[REF_FORDCS] … FORD – Charging Station
  https://www.evsolutions.com/Upload/Product/635652466512570000.pdf

## Slide 15
System/Software Architecture

## Slide 17
Implement & Verify

## Slide 19
Integrate & Validate

## Slide 21: BACKYARD
BACKYARD